BARNEGAT

TOWNSHIP

STORMWATER

MAINTENANCE

PROGRAM

May 2012

Revised: October 2015

Reviewed: May 2017

REVIEWED/REVISED MAY 15, 2017 – CME ASSOCIATES

BASIS:	Stormwater Management rules require Tier A municipalities to establish a Stormwater Facility Maintenance Program for cleaning and maintenance of all stormwater facilities operated by the municipality.  Tier A municipalities shall also clean all catch basins annually to remove accumulated sediment and debris.

GENERAL:  The Township of Barnegat’s Department of Public Works will ensure that Stormwater Facility inspections and maintenance are being undertaken, that work practices and proper conditions are met prior to beginning, during and at the conclusion of such operations.  It should not be assumed that every acceptable safety precaution is contained herein or that unusual circumstances may not require further or additional procedures, equipment and practices.  Employees will cease operations if there is a question regarding a hazard or if such is suspected or discovered.

RESPONSIBILITY:  The Superintendent of Public Works or the Municipal Stormwater Coordinator is solely responsible for all facets of this program and has full authority to make necessary decisions to ensure success of the program.  The Superintendent of Public Works and the Municipal Stormwater Coordinator are solely authorized to amend these instructions and are authorized to halt any operation not conducted in accordance with these instructions.

OPERATONS POLICY:	If shall be the goal of the Township of Barnegat to annually inspect and clean all, as needed, Township owned inlets, manholes and pipes.  Inspection and the required maintenance of the Township owned systems is spread out throughout the year, weather permitting.

Subsurface System: Inspection of subsurface systems will determine what repair or 		maintenance is needed.  Inspection and cleaning will typically be performed at the same time.  	The condition of Township owned structures will be evaluated and the information will be 	reported to the Supervisor of Public Works.  Repairs or replacement will be scheduled and 	performed as required through the Department of Public Works.  Removal of miscellaneous 	debris and sediment will be performed at the time of the inspection or will be scheduled for 	completion in a timely manner.  The top or grate portion of the inlets are cleaned of leaves and 	miscellaneous debris after heavy rains.  This allows water to enter the system without any 	obstructions and prevents pollutants from entering the storm sewer system

Surface System:  Inspection of the surface system will include functional and aesthetic needs.  	Functional maintenance is important for performance and safety reasons and aesthetic is 	important primarily for public acceptance of stormwater facilities.  The removal of debris, 	sediment, overgrown or weedy vegetation and erosion conditions will be evaluated and 	corrected.  Conditions of structures such as inlets/outlets, boxes, pipes, grate racks and 	spillways will be evaluated and reported to the Township Engineer if corrective action is 	required.

CONTENTS OF THE STORMWATER FACILITY

MAINTENANCE PROGRAM

1.	WRITTEN PROGRAM

2.	GENERAL REQUIREMENTS

3.	STORMWATER FACILITIES

4.	SURFACE ENCUMBRANCES AND UNDERGROUND INSTALLATIONS SAFETY 	GUIDELINES

5.	STORMWATER FACILITY INSPECTIONS

6.	CATCH BASIN AND PIPE CLEANING

7.	CATCH BASIN AND PIPE DEBRIS

8.	EXPOSURE TO VEHICULAR TRAFFIC

9.	WARNING SYSTEMS FOR MOBILE EQUIPMENT

10.	PERSONAL PROTECTIVE EQUIPMENT (PPE)

11.	TRAINING REQUIREMENTS

12.	MANAGEMENT PLAN CONSIDERATIONS

13.	MANAGEMENT PLAN PROCEDURE REQUIREMENTS

14.	RETROFITTING AN EXISTING STORMWATER MANAGEMENT MEASURE

15.	PRIVATELY OWNED SYSTEMS

16.	IMPROPER DISPOSAL OF WASTES

17.	STORMWATER MANAGEMENT PLAN FOR NON-PINELANDS PROPERTY

18.	STORMWATER MANAGEMENT PLAN FOR PINELANDS PROPERTY

1.	WRITTEN PROGRAM

The Township of Barnegat’s Department of Public Works will review and evaluate this 	standard practice instruction:

a.	On an annual basis

b.	When regulatory changes occur that prompt revision of this document

c.	When facility operational changes occur that require a revision of this 					document

Effective implementation of this program requires support from all levels of management within 	the Township of Barnegat.  This written program will be communicated to all personnel that are 	affected by it.  It encompasses the total workplace, regardless of the number of workers 	employed or the number of work shifts.  It is designed to establish clear goals and objectives.

2.	GENERAL REQUIREMENTS

The Township of Barnegat’s Department of Public Works will establish procedures to ensure 	that Stormwater Facility inspections and maintenance are undertaken by its employees 	through the use of this document.  Proper maintenance of stormwater facilities operated by the 	Township of Barnegat is the principle purpose of this document.  This document will provide a 	basis for ensuring that all procedures implemented, revised or modified meet our 	stormwater 	management plan.  This document will help identify stormwater facility conditions and enable 	us to determine the best course of action to take to repair or improve their operation.

2.1	The Stormwater Coordinator/DPW Superintendent shall be responsible for the 				Stormwater Management measure.

2.2	Specific preventative and corrective maintenance tasks:

2.2.1	Sediment removal

2.2.2	Trash & debris

2.2.3	Mowing

2.2.4	Pruning & restoration of vegetation

Thinning of shrubs and trees will also be performed with care to ensure that soil 				stabilization is minimally affected.

2.2.5	Restoration of eroded areas

2.2.6	Mosquito control program

Barnegat Township uses a spray truck from June through September to 					control mosquito population and breeding areas.

2.2.7	Control of aquatic vegetation

2.2.8	Repair or replacement of damaged or deteriorated components

2.2.9	Street sweeping

Maintenance of all drainage systems begins with an aggressive street 					sweeping program of all paved roadways.  The goal is to collect 						miscellaneous debris, sand and leaves before it enters the system.  This is 				done with the use of a street sweeper operating on a daily basis, weather 					permitting.

2.3	Scheduling of regular inspections and tasks for specific structural stormwater measures 			are done through the Public Works Department by work orders.

2.4	Cost estimated for maintenance tasks, including those listed under “specific 				preventative and corrective maintenance tasks” are done by Public Works.

2.5	Maintenance of equipment, tools and supplies necessary to perform the various 				preventative and corrective maintenance tasks are done by Pubic Works.

2.5.1	Sources of specialized, proprietary and nonstandard equipment, tools and 					supplies should be provided.  Vehicles and equipment used for stormwater 				maintenance:

1 Ton dump truck				1 Mechanical Sweeper

5 Ton and larger dump truck		Vac-Con jet truck

Backhoe					Wood chipper

Loader					Chainsaws

Skid Steer					Miscellaneous hand tools

DR-mower

The Department of Pubic Works will also use private contractors and/or lease 				equipment not owned by the Township to perform the required maintenance.

2.5.2	Maintenance, repair and replacement instructions for specialized, proprietary and 			nonstandard measure components including manufacturer’s product instructions 				and user manuals.

2.6	Recommended corrective responses to various emergency conditions are done by 			Public Works and the Township Engineer.

2.7	Procedures and equipment required to protect the safety of inspection and maintenance 		personnel are in our Township Safety Manual.  PPE and equipment is provided by the 			Township.

2.8	Approved disposal and recycling sites and procedures for sediment, trash, debris and 			other material removed from the measure during maintenance operations are taken to 			dry beds in Ocean Township or OCUA.

2.9	Originals or copies of manufacturer’s warranties on pertinent measure components are 			kept on file for all equipment.

2.10	As-built construction plans of the stormwater management measure and copies of 			pertinent construction documents such as laboratory test results, permits and 				completion certificates are provided by our Township Engineer and kept on file.

3.	STORMWATER FACILITIES

Stormwater facilities operated by the Township of Barnegat may include:

3.1.	Catch basins – There are currently 1536 catch basins in the Township.  Stormwater is 			conveyed to these inlets from drainage of street and gutter sections of the paved 				roadways.  Inlets within the Township are generally categorized as follows:

3.1.1	Catch Basin – a concrete box that receives stormwater through an open section 				of the curb face in the gutter section of the street

3.1.2	Grate Type Drop Box – receives stormwater directly from the gutter section

3.2.	Detention basins – Detention ponds are fed by surface or subsurface systems and are a 		vital part of our flood control (Bay area tidal flooding/storm surge) and water quality.  			These ponds are designed to include an overflow system of a box, outlet or spillway that 		carries water downstream in the event of excessive runoff conditions.  Most detention 			ponds constructed in the Township of Barnegat were designed as extended dry 				detention facilities which eventually drain after the stormwater runoff ends.  Routine 			maintenance for detention ponds includes trash and debris removal.  Mowing of both 			native and turf grass, and thinning or removal of willows, shrubs and trees are also 			included.  Written inspections of Township owned detention ponds will be done once a 			year in the spring. All work that needs to be completed on these ponds will be 				performed before summer rainfalls.  The Township will also perform visual inspections 			on all Township owned ponds after a storm event.

3.2.1	Old Main Shore - Cross street Southwind Ct.

3.2.2	Cannonball Dr. - Cross street Georgetown Blvd.

3.2.3	Bayview Blvd. - Cross street Compass Ln.

3.2.4	Barnegat Blvd. Across from Dunfee School

3.2.5	Starboard Ave. - Cross street Schooner Ave.

3.2.6	Ravenwood Blvd. - Cross street Spruce Circle South

3.2.7	Ravenwood Blvd. - Cross street Spruce Circle South

3.2.8	Fifth St.– End of Fifth St.

3.2.9	Shelli Terr. - Cross street Tara Ln.

3.2.10	Tara Ln. - Cross street Bowline St.

3.2.11	Allison Way - Cross street Burr St.

3.2.12	Pheasant Run - Cross street West Bay Ave.

3.2.13	Pheasant Run - Cross street West Bay Ave.

3.2.14	Brookville Dev. - Cross street Jon Dr. across from Jennifer Ln.

3.2.15	6 Sturgeon St. - Cross street Heritage Point Blvd.

3.2.16	42 Mission Way - Cross street Fenwick Ln.

3.2.17	65 Hatteras Way- Cross street Vineyard Way

3.2.18	35 Hatteras Way - Cross street Pierhead Dr.

3.2.19	126 Vivas Dr. - Cross street Bengal Blvd.

3.2.20	1 Plymouth Way - Cross street Marshfield Hill Blvd.

3.2.21	58 Plymouth Way - Cross street Marshfield Hills Blvd.

3.2.22	10 Salem Ct. - Cross street Marshfield Hills Blvd.

3.2.23	15 West Port Dr. - Cross street Watch Hill Ln.

3.2.24	50 Carriage Way - Cross street West Bay Ave.

3.2.25	2 Blue Claw Dr. - Cross street Hillside Ave.

3.2.26	2 Seurat St. - Cross street Tedesco Way

3.2.27	1 Freedom Hills Blvd. - Cross street Old Main Shore Rd.

3.2.28 124 Freedom Hills Blvd. - Cross street Cove St.

3.2.29	130 Mirage Blvd. - Cross street Whitewater Dr.

3.2.30	18 Hidden Lake Cir. - Cross street Bridgewater Passage

3.2.31	48 Aqua View Ln. - Cross street Whitewater Dr.

3.2.32	40 Starboard Ave. - Cross street Lamp Post Dr.

3.2.33	53 Newport (behind) - Cross street South Point Blvd.

3.2.34	2 Periwinkle Dr. - Cross street Chestnut Way Cir.

3.2.35	Across from 1 Esplanade Dr. Mirage Clubhouse

3.2.36	Behind 100 Rockrimmon Blvd.

3.2.37 Honeysuckle Dr. & Garden Path

3.2.38 Behind 57 Twilight Dr.

3.3.	Stormwater conveyances

4.	ENCUMBRANCES AND UNDERGROUND INSTALLATIONS SAFETY GUIDELINES

All surface encumbrances that are located so as to create a hazard to employees will be 	removed or supported, as necessary, to safeguard employees.  The estimated location of 	utility installations, such as sewer, telephone, fuel, electric, water lines or any other 	underground installations that reasonably may be expected to be encountered during 	excavation work, will be determined prior to opening an excavation.  The following procedures 	are designed to provide employees of Barnegat Township with a system for protection and 	safe conditions while working in an erosion control and maintenance environment.  These 	guidelines are designed for use by employees at all levels within the work force.

4.1	Establish the locations of all underground and overhead utilities and services before 			beginning erosion maintenance operations.

4.1.1	Contact utility and service companies, to include municipal owned, and advise 				them prior to the start of all actual maintenance or repair.  Call NJ ONE CALL at 				800-272-1000 for mark out of utilities.

4.1.2	The following local response times for utility companies in our area to locate and 				advise us on underground installations or surface encumbrances are as follows:

Atlantic City Electric				3 Days

NJ Natural Gas				3 Days

Barnegat Township Utilities		3 Days

Verizon Telephone				3 Days

Comcast Cable				3 Days

4.1.3	Utility companies or owners will be contacted:

a.	Within established or customary local response times;

b.	Advised of the proposed work, and;

c.	Asked to establish the location of the utility underground installations prior 					to the start of actual repair/maintenance and provide advice concerning 					surface encumbrances.

4.1.4	When repair/maintenance operations approach the estimated location of 					underground installations, the exact location of the installations will be 					determined by safe and acceptable means (modern techniques and customary 				types of equipment). Where this determination is unclear, the owning utility will 				be contacted for assistance.

5.	STORMWATER FACILITY INSPECTIONS

The Township Stormwater Coordinator and Superintendent of Public Works will oversee the inspection and maintenance of all Township owned and privately owned storm systems within the Township of Barnegat.  Visual inspections should be performed in conjunction with routine stormwater sewer system 	maintenance.  Personnel should make observations that can be used to identify contaminated stormwater, such as presence of floating and suspended materials, oil and grease, discoloration, turbidity, odor, foam or unusual vegetative growth.

5.1	If contents are discovered in any portion of the stormwater sewer system that look or 			smell suspicious like gas or oil, chemical-smelling sludge, etc. the following steps 			should be taken:

5.1.1	Keep contents isolated and do not allow it to mix with “clean” debris that has 				been removed from other locations.

5.1.2	Call Environmental Services with location, characteristics (smell, appearance) for 			further investigation.

5.1.3	Environmental Services will assist in sampling, analysis and proper disposal 				protocol once the substance is determined.

5.1.4	All confined space rules will apply as per Barnegat Township Safety Rules.

5.2	All catch basins will be inspected annually.  Inspections will be documented on the 			catch basin inspection log.  The annual inspections will also be supplemented by:

5.2.1	Routine patrol by foreman during rain event

5.2.2	Routine patrol by foreman after a rain event

5.2.3	Citizen complaints received in DPW office

5.2.4	Township of Barnegat Adopt-A-Drain Program

5.3	Inspect catch basins after any flooding or other hazard producing occurrence to 				determine if any corrective actions are needed.  A person that has the competence to 			do so will have this responsibility.

5.3.1	Utilities Manager

5.3.2	DPW Superintendent

5.3.3	Any staff deemed by Management that has the training and knowledge to 					complete inspections.

5.4	Catch basins that are determined to need maintenance through the inspection process 			will be scheduled for repairs.  The inspector will provide a recommendation for the 			repair and prevention is applicable.  Emergent conditions will be given priority for repair.

5.5	The repairs will be scheduled as soon as possible into the daily operations of the Public 			Works Department.

5.6	Detention basins will be inspected annually and after any major rain event.

5.6.1	Detention basins will also be visually inspected weekly during the mowing 					season.  Personnel assigned to cut grass in the basins will note any items 					needing repair.

5.6.2	Any detention basins found needing repairs will have the repairs scheduled as 				soon as possible.  Emergent conditions will be given priority for the repair.

6.	CATCH BASIN AND PIPE CLEANING

6.1	Basins that have been identified to need cleaning during the inspections will be 				scheduled for cleaning.  Basins will be cleaned using a truck mounted jet/vac unit.

6.1.1	Basin cleaning consists of vacuuming debris from the basin, washing down of the 			basin walls and the jetting of any debris that is located in the pipes.

6.1.2	Water used to clean the basin may be decanted back into the basin.

6.1.3	Catch basin debris will be taken to the Ocean Township drying bed/storage pad.

7.	CATCH BASIN AND PIPE DEBRIS

7.1	All debris removed from catch basins will be stored on the debris storage pad at the 			Ocean Township drying bed.

7.1.1	Debris will be stored until the pad becomes 2/3 full.

7.1.2	Debris will be tested and be waste type classified.

7.1.3	Upon DEP approval and classification, the debris will be taken to an approved 				landfill for disposal.

8.	EXPOSURE TO VEHICULAR TRAFFIC

Employees exposed to public vehicular traffic will be provided with, and will wear; warning 	vests or other suitable garments marked with or made of reflective or high-visibility material.  	Barnegat Township Police will assist in traffic control when necessary.

9.	WARNING SYSTEMS FOR MOBILE EQUIPMENT

When mobile equipment is operated adjacent to roadside basins, the vehicles amber warning 	lights must be operating.  Traffic control zones are to be established in accordance with the 	Manual of Uniform Traffic Control Devices.

10.	PERSONAL PROTECTIVE EQUIPMENT (PPE)

The following procedures are designed to provide employees of the Township with a checklist 	system or procedure to follow for the selection of proper PPE for operations under this 	program.

10.1	Checklist

10.1.1	Hard hat

10.1.2	Long sleeve garment

10.1.3	Trousers

10.1.4	Safety toe work boots

10.1.5	Proper eye and face protection

10.1.6	Work gloves, rubber or neoprene when working with or around chemicals

10.1.7	Hearing protection

10.1.8	Hi-visibility/reflective clothing

11.	TRAINING REQUIREMENTS

11.1	Initial training

11.1.1	The Township of Barnegat shall provide training to ensure that the purpose and 				function of the Stormwater Facility Maintenance Program is understood by 				employees and all affected employees acquire the knowledge and skills required 				for safe operations.  The training shall include as a minimum the following:

a.	Training in the recognition of applicable hazards associated with roadside 					maintenance operations.

b.	Each affected employee shall be instructed in the purpose and use of this 					standard practice instruction.

c.	All other employees whose work operations are or may be in an area 					where roadside maintenance operations are conducted shall be instructed 				to an awareness level about the procedures and prohibitions relating to 					work in areas.

11.2	Refresher training

11.2.1	Retraining shall be provided for all authorized and affected employees whenever 				there is a change in their job assignments, a change in equipment or processes 				that present a new hazard or when there is a change in these procedures. 					NOTE: Retraining (to include a procedural review) will also be provided 					whenever these procedures fail.

11.2.2	Additional retraining shall also be conducted whenever a periodic inspection 				reveals, or whenever the Township has reason to believe, that there are 					deviations from or inadequacies in the employee’s knowledge or use of these 				procedures.

11.2.3	The retraining shall reestablish employee proficiency and introduce new or 				revised operational methods and procedures, as necessary.

11.3	Certification: The Township of Barnegat shall certify that employee training has been 			accomplished and is being kept up to date.  The certification shall contain each

employee’s name and dates of training.

12.	MAINTENANCE PLAN CONSIDERATIONS

In addition to the plan contents, the following should also be addressed:

12.1	Access: All stormwater management measures’ components must be readily 				accessible for inspection and maintenance.  The exact limits of inspection and 				maintenance easements and rights-of-way should be specified on stormwater 				management measure plans and included in the maintenance plan.

12.2	Training of Maintenance Personnel:  Beginning with a basic description of the 				purpose and function of the overall stormwater management measure and its major 			components.  Personnel may require training in specialized inspection and maintenance 		tasks and/or the operation and care of specialized maintenance equipment.  Training 			should also be provided in the need for and use of required safety equipment and 			procedures.  This training will be administered by Management and through classes at 			Rutgers.

12.3	Aesthetics:  The impacts of the aesthetics of the stormwater management measure on 			the surrounding community should be included in the consideration for the design and 			selection of the stormwater management measure.  This is determined by the Township 		Engineer with input from the Township.

13.	MAINTENANCE PLAN PROCEDURE REQUIREMENTS

Once the maintenance plan is completed, the NJDEP Stormwater Management Rules require 	that the following procedures be followed:

13.1	Copies of the maintenance plan must be provided by the developer to the owner and 			operator of the stormwater management measure as well as the following:

13.1.1	All reviewing agencies as part of each agency’s approval process

13.1.2	Local mosquito control and extermination commission, upon request

13.2	The title and date of the maintenance plan and name, address and telephone number of 		the person with stormwater management measure maintenance responsibility as 				specified in the plan must be recorded on the deed of the property on which the 				measure is located as well as any changes of information.

13.3	The person with maintenance responsibility must:

13.3.1	Evaluate the maintenance plan for effectiveness at least annually and revise as 				necessary.

13.3.2	Keep detailed, written logs of all preventative and corrective maintenance 					performed at the stormwater management measure including a record of all 				inspections and copies of maintenance-related work orders.

13.3.3	Retain and, upon request, make available the maintenance plan and associated 				logs and other records for review by the public entity with administrative, health 				environmental or safety authority over the site.

14.	RETROFITTING OF EXISTING STORMWATER MANAGEMENT MEASURES

Retrofitting can be defined as expanding, modifying or otherwise upgrading existing 	stormwater management measures.  Retrofitting facilities built to control stormwater quantity 	impacts of 10-year, 25-year and/or 100-year storms to also control smaller storm events that 	are typically responsible for the majority of stormwater quantity and streambank erosion will 	address problems that may not have been previously addressed.  Another important benefit of 	retrofitting stormwater management facilities is the opportunity to correct site nuisances, 	maintenance problems and aesthetic concerns.

In addition to such basic considerations as need and cost, three important factors must be 	considered when evaluating retrofit possibilities:

14.1	Health and safety:  A retrofit must not increase health or safety risks in any way

14.2	Effectiveness:  Performance improvements for a range of retrofits must be evaluated 			to determine which one represents the optimum combination of effectiveness, viability 			and cost.  The final retrofit selected for an existing stormwater measure will have to be 			based on its relative rather than absolute effectiveness.

14.3	Maintenance:  Factors that can cause increases in the level, frequency, complexity 			and/or cost of the present inspection and maintenance efforts performed at the 				stormwater management measure:

14.3.1	It should be expected that if a retrofit will increase a stormwater management 				measure’s pollutant removal capability, it will also increase the rate and total 				volume of sediment, trash, debris and other stormwater pollution that will 					accumulate in the measure.

14.3.2	The chemical or biological composition of this sediment may be of a significantly 				power quality and potentially either hazardous or toxic that the sediment 					previously captured.

14.3.3	The retrofit may increase the number and/or complexity of components in an 				existing stormwater management measure.

14.4	Private Storm Drain Inlet Retrofitting (Ordinance #2010-13):  It is required that the 			retrofitting of existing storm drain inlets which are in direct contact with repaving, 				repairing, reconstruction or resurfacing or alterations of facilities on private property, to 			prevent the discharge of solids and floatables (sediment, debris, trash and other 				floating, suspended or settleable solids) to the municipal separate storm sewer 				system(s) operated by the Township of Barnegat so as to protect public health, safety 			and welfare and to prescribe penalties for the failure to comply.

Increased staffing, improved equipment and/or specialized training may be required to properly 	maintain the new retrofitted measure.  Therefore, the extent and impacts of any increased 	inspection and/or maintenance requirements should be determined and thoroughly evaluated.

Community education should also be considered as a retrofit component.

15.	PRIVATELY OWNED SYSTEMS

The Township of Barnegat will ensure that the maintenance and cleaning of all privately owned 	storm systems within the Township is in compliance.  Owners of private facilities are required 	to clean and perform any necessary repairs to all inlets, manholes, underground pipe, 	channels and detention ponds on their property.  After work is complete, all facilities will be 	inspected by the Township of Barnegat’s Stormwater Supervisor for compliance.

15.1	Maintenance Requirements:  Responsibility for operation and maintenance facilities, 			including periodic removal and disposal of accumulated particulate material and debris, 			shall remain with the owner or owners of the property with permanent arrangements 			that it shall pass to any successive owner, unless assumed by a government agency.  If 		portions of the land are to be sold, legally binging arrangements shall be made to pass 			the basic responsibility to successors in title.  These arrangements shall designate for 			each project the property owner, governmental agency or other legally established 			entity to be permanently responsible for maintenance, hereinafter referred 	to as the 			“responsible person” (Land Use Code 55-326 - Ordinance 1990-4).

15.2	Danger to public safety or public health:  In the event that the stormwater management 			facility becomes a danger to public safety or public health, or if it is in need of 				maintenance or repair, the municipality shall notify the responsible person in writing.  			Upon receipt of that notice, the responsible person shall have fourteen (14 days) to 			affect maintenance and repair of the facility in a manner that is approved by the 				Municipal Engineer or his designee.  The municipality, in its discretion, may extend the 			time allowed for effecting maintenance and/or repair for good cause.  If the responsible 			person fails or refuses to perform such maintenance and/or repair, the municipality or 			County may immediately proceed to do so and shall bill the cost thereof to the 				responsible person (Ordinance 2006-08, Sec. 55-329-10 of Barnegat Township Land 			Use Code Book)

15.3	Emergency Requests: Emergency requests for assistance with drainage problems, 			such as flooding, on private property will be responded to immediately.

15.4	Routine Requests: Routine requests for maintenance or alterations of storm systems 			on private property will be inspected, evaluated and approved or denied on a case by 			case basis by the Township Stormwater Supervisor or Township Engineer.

16.	IMPROPER DISPOSAL OF WASTES

The spilling, dumping or disposal of materials other than stormwater in such a manner as to 	cause the discharge of pollutants to the municipal separate storm sewer system is prohibited.

17.	STORMWATER MANAGEMENT PLAN FOR NONPINELANDS PROPERTY

Refer to Barnegat Township Land Use Code Book Section 55-329

18.	STORMWATER MANAGEMENT PLAN FOR PINELANDS PROPERTY

Refer to Barnegat Township Land Use Code Book Section 55-330